## Slide 1
TEACHERS' WORKSHOP
SMART LIGHT SENSOR
Automatic Night Light using LDR, Arduino Uno and LED
Made by Sir Anwar Siraj, DS & AI Robotics
For Teachers

## Slide 2: What Does This Project Do?
DARK ROOM
LDR resistance goes UP, the reading goes DOWN, and the LED turns ON automatically.
BRIGHT ROOM
LDR resistance goes DOWN, the reading goes UP, and the LED turns OFF.
How the signal travels
Light
LDR senses the brightness
Pin A0 reads 0 to 1023
Code compares with threshold
Pin 13 switches LED ON / OFF

## Slide 3: Components We Need
1
Arduino Uno
x 1
The brain of the project
2
USB Cable
x 1
Gives power and uploads code
3
Breadboard
x 1
Connect parts, no soldering
4
LDR
x 1
Light sensor with 2 legs
5
Resistor 10 kΩ
x 1
Bands: brown, black, orange
6
LED (any color)
x 1
Lights up in the dark
7
Jumper Wires
x 4
Red, yellow, black + spare
8
Resistor 220 Ω
optional
Protects LED: red, red, brown

## Slide 4: LDR Full Form
L
LIGHT
The brightness around us: room light, sunlight, a torch or a lamp falling on the sensor.
D
DEPENDENT
It depends on the light: its behavior changes according to how much light it receives.
R
RESISTOR
A part that resists (slows down) the flow of electric current. Measured in ohms (Ω).
LDR = a resistor whose resistance changes with light
Dark: resistance HIGH | Bright: resistance LOW

## Slide 5: The LDR: Light Dependent Resistor
LEG 1
LEG 2
Curvy track = light-sensitive material
1
2 legs, no polarity
Either leg can go to 5V or to A0. There is no wrong way round.
2
Bright light = low resistance
Resistance drops to roughly 1 kΩ.
3
Darkness = high resistance
Resistance rises above 100 kΩ.
4
Our wiring
Leg 1 to 5V (positive). Leg 2 to A0 and to the 10 kΩ resistor.

## Slide 6: Meet the Other Components
Resistor 10 kΩ
No polarity: either way works
Works with the LDR as a voltage divider
One leg joins the LDR junction, the other leg goes to GND (negative)
LED
Has polarity: long leg is positive (+)
Long leg to pin 13, short leg to GND (−)
Wrong way round = it will not light
UNO
Arduino Uno
5V pin = positive power for the LDR
GND pin = negative (0 V) return
A0 reads 0 to 1023, pin 13 drives the LED

## Slide 7: How It Works: Voltage Divider
The LDR and the 10 kΩ resistor share the 5 V. Arduino measures the voltage at the middle point (A0).
V(A0) = 5 V × 10 kΩ ÷ (R_LDR + 10 kΩ)
0 – 1023
analogRead() range (0 V to 5 V)
BRIGHT
LDR resistance LOW → A0 voltage HIGH → reading is high (for example 600) → LED OFF
DARK
LDR resistance HIGH → A0 voltage LOW → reading is low (70 or less) → LED ON

## Slide 8: Why Does the LED Turn ON in the Dark?
ONE WORD:
VOLTAGE
Resistance goes UP, so the voltage at A0 goes DOWN.
The LDR is on the 5V side. When it resists more, it uses more of the 5V, so less voltage is left at A0.
1
Dark: LDR resistance goes UP
2
Voltage at A0 goes DOWN
3
Reading becomes 70 or less (threshold)
4
if() is true: pin 13 HIGH, LED ON

## Slide 9: Circuit Diagram (Schematic)
5V (+)
Leg 1
Leg 2
LDR
A0 analog pin
10 kΩ
GND (−)
Pin 13
LED
long leg (+)
short leg (−)
Tip: add a 220 Ω resistor in series with the LED to protect it.
Red = 5V (+)
LDR Leg 1 connects here
Yellow = signal
LDR Leg 2 + resistor meet at A0
Black = GND (−)
Resistor free leg goes here
Green = output
Pin 13 to LED long leg

## Slide 10: Physical Circuit: Arduino + LDR + LED
5V (+)
A0 junction
GND (−)
LDR
Leg 1
Leg 2
10 kΩ
GND
13
5V
A0
GND
ARDUINO UNO
(simplified drawing: read the pin labels on your board)
LED
short leg (−)
long leg (+)
Red wire
5V (+) to the strip with LDR Leg 1
Yellow wire
A0 to the strip where LDR Leg 2 and the resistor meet
Black wire
GND (−) to the strip with the resistor free leg
LED
Long leg to pin 13, short leg to GND

## Slide 11: Step-by-Step Wiring
1
Power off
Unplug the USB cable before wiring.
2
Place the LDR
Put its 2 legs in two different breadboard strips (no polarity).
3
Place the 10 kΩ resistor
One leg shares the strip with LDR Leg 2, the other leg goes in a new strip.
4
Red wire: 5V (+)
Arduino 5V to the strip of LDR Leg 1.
5
Yellow wire: A0
Arduino A0 to the strip where LDR Leg 2 and the resistor meet.
6
Black wire: GND (−)
Arduino GND to the strip of the resistor free leg.
7
Add the LED
Long leg to pin 13, short leg to the GND pin next to it.
8
Upload and test
Plug in USB, upload the code, open Serial Monitor at 9600.

## Slide 12: The Code
// CODE
// MADE BY SIR ANWAR SIRAJ, DS & AI ROBOTICS
int ldrPin = A0;
int led = 13;
int threshold = 70;
void setup()
{
Serial.begin(9600);
pinMode(led, OUTPUT);
}
void loop()
{
int data = analogRead(ldrPin);
Serial.println("");
Serial.print("Light Sensor ");
Serial.print("Value = ");
Serial.print(data);
if(data <= threshold)
{
digitalWrite(led, HIGH);
}
else
{
digitalWrite(led, LOW);
}
}
1
Variables
ldrPin = A0, led = 13 and threshold = 70 are names and numbers we choose.
2
setup() runs ONCE
Starts the Serial Monitor and makes pin 13 an output for the LED.
3
loop() repeats FOREVER
Read the LDR, print the value, compare with threshold, switch the LED.

## Slide 13: Code Explained Line by Line
Code | What it means
int ldrPin = A0; | The LDR signal wire is connected to analog pin A0.
int led = 13; | The LED is connected to digital pin 13.
int threshold = 70; | The dividing line between dark and bright (scale 0 to 1023).
Serial.begin(9600); | Starts the Serial Monitor at speed 9600.
pinMode(led, OUTPUT); | Pin 13 sends power OUT to the LED.
analogRead(ldrPin) | Reads A0 and gives a number 0 to 1023, saved in data.
Serial.print(...) | Shows "Light Sensor Value = number" on the screen.
if(data <= threshold) | Dark? LED ON (HIGH). Otherwise else: LED OFF (LOW).

## Slide 14: What is Threshold? Why Do We Need It?
IN SIMPLE WORDS
Threshold = the decision line
A limit number. On one side of it one thing happens, on the other side something else happens.
Example: If marks are 40 or more you PASS, otherwise FAIL. Here 40 is the threshold. In our project: reading 70 or less = DARK, LED ON.
Why is threshold needed?
1
Arduino reads only numbers (0 to 1023). It does not know the words dark or bright.
2
Threshold tells Arduino which number means dark.
3
Without it, the LED cannot decide when to turn ON or OFF.
4
We chose 70 by testing in our room. Light differs, so you can change it.

## Slide 15: What Do 70 and 1023 Mean?
0
means 0 V (no voltage)
1023
means 5 V (full voltage)
No unit
It is only a count: 1024 steps, about 0.0049 V each
Reading | Voltage at A0 | Meaning
0 | 0 V | Darkest possible
70 | 0.34 V | DARK: our threshold
512 | 2.5 V | Medium light
1023 | 5 V | Brightest possible
Formula: Voltage = reading × 5 ÷ 1023 (70 × 5 ÷ 1023 = about 0.34 V)

## Slide 16: How to Choose the Threshold (4 Steps)
1
Open Serial Monitor
Connect USB, upload the code, set speed to 9600.
2
Find the DARK number
Cover the LDR with your finger. Note the number (example: 40).
3
Find the BRIGHT number
Shine a torch or room light. Note the number (example: 600).
4
Pick a number in between
Choose near the dark value (example: 70). Write it in int threshold = 70; and upload.
Example numbers only: your readings will be different in your room.
LED turns ON too late? Raise the threshold. LED ON even in daylight? Lower the threshold.

## Slide 17: Threshold: Dark or Bright?
0 to 70
DARK = LED ON
71 to 1023
BRIGHT = LED OFF
threshold = 70
(bar not to scale)
1
What is it?
A number we choose from 0 to 1023. If the reading is 70 or less, the room is "dark enough" and the LED turns ON.
2
Tune it
Raise it to 200: the LED turns on in dim light. Lower it to 30: the room must be very dark. Watch the Serial Monitor and pick your value.
3
Test it
Cover the LDR with a finger: the number falls and the LED turns ON. Shine a torch: the number rises and the LED turns OFF.
Troubleshooting: LED never lights? Check LED direction and pin 13. Number stuck at 0 or 1023? Check the 10 kΩ resistor and the A0 wire.

## Slide 18
What We Learned
1
The LDR has 2 legs and no polarity: its resistance changes with light.
2
LDR + 10 kΩ resistor make a voltage divider; A0 reads the middle point.
3
analogRead gives 0 to 1023; threshold = 70 decides dark or bright.
4
if / else turns the LED ON in the dark and OFF in the light.
TRY IT
Change the threshold to 200
Use a different LED pin
Make the LED blink in the dark
Add delay(200) to slow the Serial Monitor
Made by Sir Anwar Siraj, DS & AI Robotics, for Teachers